## Slide 1
IoT SMART DRYING
CHAMBER MONITORING SYSTEM
A first prototype for an AI-based agricultural produce quality and drying project
Presented by: [Your Name]
Department: CSE (AIML) | REVA University
Project proposal • Prototype plan • Not yet a completed system
1

## Slide 2
1. Project overview
What we plan to build in the first prototype
2
IoT Smart Drying Chamber | Project Proposal
Measure
Read temperature and relative humidity inside a small drying chamber.
Connect
Send sensor readings from the ESP32 to a live dashboard over Wi-Fi.
Respond
Optionally switch a low-voltage fan when conditions cross set limits.
Long-term direction: extend the chamber with a camera, validated moisture measurements, and AI models to estimate produce dryness and detect visible colour changes.
Important: the first milestone monitors chamber conditions; it does not yet measure produce moisture or discoloration directly.

## Slide 3
2. Problem statement
Why monitor a drying process?
3
IoT Smart Drying Chamber | Project Proposal
• Drying conditions can change with weather, airflow, loading, and time.
• Manual checking may not provide continuous records of temperature and humidity.
• Uneven or unsuitable drying conditions can affect drying time and product quality.
• A small connected prototype can collect data and make the process easier to observe.
Current approach
Occasional manual checks; limited automatic logging.
Proposed approach
Continuous sensor readings, a dashboard, and optional fan control.
Goal: improve visibility and data collection—not claim guaranteed food quality.

## Slide 4
3. Objectives and scope
A realistic first milestone, followed by future upgrades
4
IoT Smart Drying Chamber | Project Proposal
Phase 1 — IoT prototype
• Measure chamber temperature and humidity • Display readings on a web dashboard • Record timestamped readings • Add optional low-voltage fan control • Test sensor response under different conditions
Future phase — AI quality monitoring
• Capture images of agricultural produce • Track visible colour changes using computer vision • Add reference moisture measurements for model training • Explore thermal or NIR sensing if justified • Validate model predictions on new samples
Scope discipline: AI, camera-based discoloration detection, and direct product-moisture estimation are future extensions—not features of the basic sensor kit.

## Slide 5
4. System architecture
How information moves through the prototype
5
IoT Smart Drying Chamber | Project Proposal
DHT-type sensor
Temperature + RH
ESP32
Reads data; applies rules
Wi-Fi
Sends readings
Dashboard
Live values and trend charts
Fan driver + DC fan
Optional control output
Control rule
If threshold reached, switch fan
Dashboard options: a simple local webpage, or a beginner-friendly IoT dashboard. Internet access is needed only if the chosen dashboard is cloud-hosted.

## Slide 6
5. Components and their roles
Core parts for the first working build
6
IoT Smart Drying Chamber | Project Proposal
ESP32 DevKit
Controller; built-in Wi-Fi
DHT22 / compatible sensor
Measures temperature and relative humidity
5 V DC fan
Moves air through the chamber
MOSFET driver
Switches fan without overloading ESP32 GPIO
Breadboard + wires
Temporary circuit assembly
USB cable + supply
Programming and safe low-voltage power
Small enclosure + mesh tray
Holds sample produce and creates airflow path
The 37-sensor kit may supply useful extras, but check its exact contents; it does not replace the ESP32, fan, chamber, and power items.

## Slide 7
6. Working principle
Step-by-step operation
7
IoT Smart Drying Chamber | Project Proposal
1
Power on
ESP32 starts and connects to Wi-Fi.
2
Read sensor
Temperature and humidity are sampled at intervals.
3
Publish data
Values are sent to the dashboard with a timestamp.
4
Check limits
Controller compares readings with chosen thresholds.
5
Control fan
If enabled, the driver switches the DC fan.
6
Review trends
User checks whether conditions change over time.
Thresholds must be selected and tested for the intended produce; there is no single safe setting for every crop.

## Slide 8
7. Software and tools
Beginner-friendly development workflow
8
IoT Smart Drying Chamber | Project Proposal
Arduino IDE
Write and upload ESP32 firmware.
Serial Monitor
Check readings and debug sensor wiring.
Web / IoT dashboard
View live values and charts.
• Firmware: Arduino framework for ESP32 (C/C++ style).
• Dashboard: begin with a simple local webpage or a supported IoT dashboard.
• Data logging: store timestamp, temperature, humidity, fan state, and notes.
• Future AI: Python, OpenCV, and a model framework after collecting labelled samples.

## Slide 9
8. Data collection and testing plan
Show your teacher how you will verify that it works
9
IoT Smart Drying Chamber | Project Proposal
Data to record
• Timestamp • Temperature (°C) • Relative humidity (%) • Fan state (ON/OFF) • Sample type and setup notes • Optional reference thermometer/hygrometer readings
Tests to perform
• Compare sensor readings with a reference instrument • Check readings at room conditions and during safe airflow tests • Confirm dashboard updates at the expected interval • Verify fan switches only when commanded • Check reconnect behaviour after Wi-Fi interruption • Repeat tests and note errors
Success criteria: readings are visible, timestamps are recorded, dashboard updates reliably, and fan control behaves as designed. Report actual results only after testing.

## Slide 10
9. Safety and limitations
Design the first prototype for safe, repeatable experiments
10
IoT Smart Drying Chamber | Project Proposal
• Keep the ESP32 and exposed electronics outside the hot, humid chamber.
• Use low-voltage DC for the beginner prototype; avoid exposed mains AC wiring.
• Do not power a fan directly from an ESP32 GPIO pin—use a suitable driver.
• Check the sensor's temperature and humidity limits before testing.
• A chamber humidity sensor measures air conditions, not the exact moisture content inside the food.
• Colour change detection requires image capture, controlled lighting, and labelled examples.
Key limitation
The first prototype monitors the drying environment. Direct moisture prediction and AI-based quality classification require additional sensors, data, and validation.

## Slide 11
10. Future development roadmap
How the IoT prototype can support the larger research project
11
IoT Smart Drying Chamber | Project Proposal
Phase 1
IoT chamber
Temperature, humidity, dashboard, fan control
Phase 2
Data logging
Collect repeatable drying runs and reference measurements
Phase 3
Computer vision
RGB images under consistent lighting; colour/defect features
Phase 4
AI model
Train and validate dryness/colour models using labelled data
Phase 5
Multimodal system
Consider thermal/NIR sensing only if useful and affordable
Self-learning should mean a controlled update/retraining process using newly labelled and validated data—not automatic learning without checks.

## Slide 12
11. Estimated prototype budget
Approximate India retail prices; confirm before purchasing
12
IoT Smart Drying Chamber | Project Proposal
Item | Estimated cost
ESP32 DevKit | ₹350–₹600
DHT22 or compatible sensor | ₹200–₹350
5 V DC fan | ₹100–₹200
MOSFET driver module | ₹80–₹200
Breadboard + jumper wires | ₹180–₹330
USB cable / compatible supply | ₹150–₹300
Enclosure + mesh tray | ₹300–₹950
Expected total
About ₹1,360–₹2,930 (depending on parts already available)
Potential savings: reuse an existing enclosure, USB cable, or breadboard.

## Slide 13
12. Conclusion
What this first milestone demonstrates
13
IoT Smart Drying Chamber | Project Proposal
Connected sensing
Measure and transmit chamber temperature and humidity.
Monitoring + control
Visualise trends and optionally control a low-voltage fan.
Foundation for AI
Create a reliable data-collection base for future produce-quality research.
The immediate aim is a working, tested IoT prototype. The larger vision is to combine environmental data, images, and validated measurements to study drying and quality.
Thank you • Questions?

## Slide 14
Presenter guide: how to explain it
Use these simple points while presenting
14
IoT Smart Drying Chamber | Project Proposal
• Start: “I am proposing a small IoT drying chamber as the first step toward my agricultural AI project.”
• Problem: explain that temperature and humidity change during drying, and manual checks do not give continuous data.
• Solution: describe the sensor → ESP32 → Wi-Fi dashboard flow, then explain optional fan control.
• Components: explain the role of the ESP32, temperature/humidity sensor, fan driver, fan, and chamber.
• Testing: say you will compare readings, check dashboard updates, and test fan control before reporting results.
• Future work: explain that camera-based colour analysis and product-moisture estimation need more data and validation.
• Be clear: call this a proposed prototype until you have built and tested it; do not present planned features as completed.